DRAFTING Urban Design Guidelines meeting 3/4/2011

Overall Plan Goals Related to Design (paraphrased from the Sector Plan):

- The Crossroads is an attractive, comfortable, vibrant destination for multicultural dining and shopping.

- Unique environmental features are protected and improve in quality.

- Buildings and public space are accessible and facilitate mobility, relationship-building, and economic activity.

- Create and improve park properties within the Plan area.

- Quality public and quasi-public spaces create a sense of place and safety.

- Development is the most intense at the Purple Line Station and along University Boulevard.

- An appropriate transition occurs between the single-family community and areas of commercial activity.

- Residents and visitors conveniently and safely walk, bike and use transit to access community centers, work and shop.

- The Crossroads streets are complete streets with sidewalks, curbs, pedestrian oriented lighting, landscaping, and other improvements.

Mar 17 Goals for Discussion:

Residents and visitors conveniently and safely walk, bike and use transit to access community centers, work and shop.

The Crossroads streets are complete streets with sidewalks, curbs, pedestrian oriented lighting, landscaping, and other improvements.

The Crossroads is an attractive, comfortable, vibrant destination for multicultural dining and shopping.

Quality public and quasi-public spaces create a sense of place and safety.

Note:  See online schedule for addition topics

Rough draft text follows.

# SITE DESIGN

Intent:  Improve environmental performance of the site.

- Incorporate adequate space for operational recycling and maintenance, including space for collection, storage, and access for collection vehicles.

- Organize building mass, orientation and outdoor spaces to provide efficient pedestrian and access to services.

- Incorporate recreational areas that have multiple functions in addition to visual value.

- Coordinate landscape design with building envelope design. Orient building, windows, and outdoor spaces to work together, taking advantage of light, air flows, and interesting views.

- Consider placing renewable energy sources onsite.

## Neighborhood Compatibility

Intent:  Restrict uses in transition areas to those uses compatible with a low traffic volume single-and multi-family community.

- The uses within buildings that confront a street of properties zoned for single family or multi-family are restricted to residential or office uses with the following exception:

  - Neighborhood-service oriented commercial or institutional uses such as a dry cleaner, a corner store with a tenant foot print less than 2,000 square feet or a child day care are appropriate for street intersections.

- Uses within 150 feet of a single family or multi-family zoned property may not include a drive-through or outdoor automobile service facility.

## Focal Points

Intent: Enhance the visual and aesthetic experience of living in adjoining neighborhoods and entering the commercial district.

- Exceptional site planning and architectural design attention should be paid to focal points (corners and view termini found at local and major street intersections) in order to enhance the neighborhood/district experience and the approach to the planned project.

## Setbacks and Build-to Lines

Intent: Protect and enhance the visual and aesthetic experience of living in the New Hampshire Gardens neighborhood.

- A building confronting the primary face of single-family residential structure shall have a front setback of 25 feet from the property line or public improvement easement edge whichever is furthest from the street curb.

- A building confronting a secondary face of a single-family residential structure shall have a front setback of 10 feet from the right-of-way or public improvement easement line whichever is closest.

- Buildings shall be setback 25 feet from all single-family zoned property lot lines.

  - Any existing parking spaces located within this yard shall be allowed to remain, so long as they are screened to a height of six feet by a masonry wall and the parking is upgraded to meet landscaping requirements.

- Entrance features such as stoops, open porticos or porches may be located within the front setback so long as they are open and not enclosed.

- Driveways, parking, and accessory buildings shall not be located in the front setback.

- Building located on retail-oriented-streets, avenues or boulevards shall be built to or within five feet of the right-of-way or edge of the public-improvement-easement, whichever is furthest from the curb.

## Circulation and Access

Intent:  Create a high quality pedestrian and bicycle friendly environment that encourages alternative modes of transportation and reduces dependence upon cars.

- Large properties shall be divided into blocks a maximum of 400 feet in length.

- Parking for residential and office uses confronting the primary face of residential structures shall be accessed from an alley or a shared entrance off a side street and shall not be accessed from a primarily residential street.

- Circular, U–shaped and other driveway or pull-in features are not permitted.

- Sidewalks shall not be made of asphalt.

- Pedestrian and bicycle pathways shall have a continuous pattern and design across driveway entrances and shall not exceed 2% in cross slope.

- Sites greater than four acres in size shall have private alleys providing the access to the rear of buildings, loading, parking, dumpsters, and service entrances.

- Access to parking and loading on adjacent properties should be shared.

- Provide pedestrian and bicycle access across large commercial properties from residential neighborhoods.

- Sidewalks a minimum of five feet in width shall connect to dwelling places, parking, recreational facilities, auxiliary buildings, recycling, and dumpster areas.  Onsite, on primarily commercial properties, sidewalks shall be six feet in width.

Intent: Protect residential neighborhoods from negative impacts of commercial activity.

- Drive-thru services shall be located only on the rear of a building.

- Drive-thru services or their access drive aisles shall not be located in buildings or on land adjacent to single family or multi-family residentially zoned properties.

Intent:  Provide a quality and comfortable microclimates using solar orientation and prevailing winds.

- Orient new streets on the diagonal to the compass (SW to NE and NW to SE) where feasible.

## Screening and Buffering

Intent:  Reduce negative visual and noise impacts of new uses and buildings.

- Walls screening parking shall have a maximum height of 4 feet and shall be opaque when located on a sidewalk.  Walls screening parking from a single-family residential property shall be 6 feet in height and opaque.

- Barbed wire, vinyl cladding, unclad cinder block, or razor wire shall not be used as walls, fences, or screening.

- Chain link fence shall not be used as walls, fences, or screening, with the exception of enclosures for recreational courts (e.g. basketball).

- Dumpsters, recycling areas, HVAC units and utilities shall be screened.

      - Dumpsters, trash and building recycling containers should be located on the side of or behind a building; these shall not be located in front of a building or adjacent to a rear public entrance.

      - HVAC units shall be located either on the side of or behind a building or on top of a building to the rear or behind a parapet wall or other façade or roof treatment; these features shall not be located in front of a building or adjacent to a rear public entrance.

      - Appropriate screening materials shall be wood, brick, stone or any combination thereof that complements the main structure.

- Dumpsters on adjacent properties should be consolidated whenever possible.

- Parking adjacent to from any street public or private shall be screened by plantings a maximum of four feet in height.

- Parking garages adjacent to a public right of way or private street shall be screened by hedges, fastigate trees, vines, or a green (living) wall.

# ARCHITECTURE

## Height

Intent: Protect and enhance the visual and aesthetic experience of living in the New Hampshire Gardens neighborhood.

- New development on the properties east of New Hampshire Avenue and south of Merwood Drive may not exceed 60 feet in height.

- Buildings that confront the primary face of single family residential buildings shall have a height restricted to 40 feet for the first 25 feet of the building’s width.

- Buildings that face Kennewick Avenue shall not exceed 50 feet in height for the first 25 feet of the building’s width.

- On properties sharing a lot line with a single family home, buildings shall not exceed 35 feet measured from an average elevation of the adjacent rear yard(s) of the adjoining single-family home(s) property line(s).  This height restriction shall be applied within the first 50 feet of the lot line.  The subsequent 50 feet from the single family lot line may include an additional story.

## Massing and Building Articulation

Intent:  Create quality public and quasi-public spaces framed by buildings that enhance the visual interest and aesthetic experience of the Crossroads community.

- With the exception of structures serving primarily an institutional function, large buildings (that exceed 60 feet in street frontage, that are primarily horizontal in composition, that exceed a 1:1 ratio) shall be articulated so as to read as multiple buildings through a combination the following:

  - Massing changes:  change both the facade set back a minimum of five feet and height a minimum of two feet.

  - Material changes:  divide the building into vertical bays that use varied materials and colors.

  - Vocabulary changes:  including varying the details such as columns, window frames, types of windows, or height and shapes of windows and doors, the cornice, roofline, or pediment, the relationship of solids to voids, the relationship of projections to recesses, and the vertical and horizontal bands, so that the building and its bays are understood as several different buildings.

- Trademark buildings shall not be allowed unless they conform to the design guidelines.

- Detail and complexity is encouraged on the ground floor pedestrian level such as column, cornice, entrance, and window frame design, detail and material.

- Building designed to serve a primarily institutional function shall be of exceptional design and quality.

- Materials (limit types of materials?),

## Lighting

Intent: Promote community comfort, safety and sociability while reducing environmental impact.

- Fixtures shall be located and shielded so that light does not spill from a parking lot onto an adjacent residential property.

- Entrances shall be well illuminated with directed shielded light.

- Where feasible and appropriate consider limiting floor plans to 56 ft. or less to reduce the need for constant electric lighting.

- Incorporate daylight with light shelves, prismatic glazing and other reflective systems to extend naturally lit interior space.

- Use atria and outdoor courtyards to increase the variety and number of views.

## Openings

Intent: Promote community comfort, safety and sociability.

- The primary entrance to commercial and residential units shall be located on a public or private street, alley or a plaza and may not face a parking lot or drive aisle.

- The main entrance of building(s) shall be located on the primary pedestrian street; buildings facing two streets shall have prominent entrances on both streets or the corner.

- Corner buildings should orient entrances to the corner.

- Ground level housing and commercial units adjacent to a sidewalk should also have a separate entrance onto the sidewalk.

- Main entrances shall be highlighted with a minimum of three design elements such as an address, awnings, a portico, architectural recesses, windows (transom and sidelights), plantings, and architectural details.

- All facades shall have a minimum of 20% fenestration on all stories, including those facing the rear, alley, driveways, parking lots or other open areas.

- Multifamily buildings shall have transparent lobby and entrance windows facing the street.

- Windows facing single family residential shall be primarily vertical in character and may not be a solid glass curtain wall.

- Security grills shall not primarily be composed of vertical bars.

- Covered arcades likely to capture pollution emitted by vehicles are to be avoided in close proximity to heavily trafficked roadways.

# PUBLIC AND QUASI-PUBLIC SPACE

## Streetscape

Intent:  Provide a quality, ADA compliant pedestrian environment for walking, shopping, and socializing.  Build a unique “feel” through streetscaping to distinguish the Crossrods from any other regional shopping district.

- Overhead wires shall not be located within the streetscape for streets, avenues or alleys and shall be relocated to the rear of the building, alley or undergrounded.

- Public Utility Easements shall be located within the right-of-way or Public Improvement Easement if required and not between the streetscape or future streetscape and the building.

- Retail streets, avenues and boulevards (public or private) shall have a streetscape located between the build-to-line (the edge of the public right-of-way or public improvement easement furthest from the curb) and the curb.  This streetscape will generally be 15 feet in width with the exception of University Boulevard which shall be 25 feet in width.

  - Paving materials and pattern shall be consistent with a design selected for and associated with each avenue and boulevard.

    - Paving materials and design shall be ADA compliant.

    - Brick pavers shall be composed of clay.

    - Unique colors and patterns are encouraged, and once set for a street or block, any subsequent project shall use the established and approved design within the following framework:

      - A patterned “shy zone” shall be installed within the first two feet of the build to line.

      - A minimum seven-foot wide pedestrian “clear zone” shall be maintained between the “shy zone” and the “street furniture zone” and which shall be smooth with no grooves or bevels (non-vibration causing) for ADA compliance.

      - A “street furniture/landscape zone” which may be patterned and shall occupy the area between the “clear zone” and the street curb or cycle track.

  - On University Boulevard a cycle track of minimum 8 feet in width with a two foot green buffer (total a minimum of10 feet wide) shall be located between the boulevard curb and the street trees.

  - On University Boulevard, the streetscape/landscape zone should be more heavily landscaped than hardscape and is encouraged to include stormwater infiltration facilities.

- Non-retail oriented streets and avenues shall have a sidewalk of 8 feet in width at the edge of the right-of-way or public-improvement-easement, whichever is furthest from the curb.

- Non-retail oriented streets and avenues are encouraged to install a landscape strip with a green stormwater infiltration facility between the sidewalk and the curb.  Stepping stones or other non-continuous pavers shall be placed at regular intervals to connect the sidewalk to any on-street parking if present.

- Sidewalks shall not be made of asphalt.

- See also landscaping and hardscape requirements.

## Parks and Plazas

Intent: Create social outdoor rooms through a series of inviting and comfortable greens, plaza, and pocket parks and connected by leafy corridors and pathways.

- Where appropriate, animate public space with adjacent activating uses such as retail or restaurants.

- Parks and open space should be at grade with adjacent sidewalks and shall be no more than three steps above or below grade.

- Include artwork as an integrated design element on the walls, floors and ceilings of outdoor space. Promote participatory artwork that moves or responds to the viewer, creates mystery or whimsy.

- Fountains are strongly encouraged, especially in hardscaped areas.

- Consider incorporating elements that are climbable and which also function as seating such as rocks, seating walls, steps, and public art.

## Yards, Patios and Courtyards

- Residential units are strongly encouraged to incorporate usable semi-private outdoor space that has a visual connection with the street, such as porches, stoops, balconies, and terraces.

- Residential or office terraces, courtyards, and gardens adjacent to a street sidewalk shall not be enclosed by a wall or include a gate that exceeds three and a half feet in height.

- Residential yards, grounds, and open space shall be attractively planted with a variety of shrubs, ground cover and trees.

- Design courtyards with a central feature such as a fountain.

- Ground level or rooftop community gardens are strongly encouraged.

- Trellises are encouraged on upper story outdoor spaces.

- Consider placing basketball and other sport playing facilities on rooftops.

- Where feasible, include facilities for residential composting.

## Lighting

Intent:  Use site furniture to create a unique visual identity for the crossroads and create a comfortable and safe evening environment.

- Pedestrian-oriented lights shall be located every 70-90 feet in the street furniture zone or landscape strip and along public and quasi-public walkways.

  - Luminaires shall be located no more than 10 feet in height on non-retail streets and no lower than 12 feet on retail streets.

  - Poles shall be aluminum with pendant style lights with a wide shade.

  - Design shall be consistent across the Crossroads shopping district and as specified in these documents.

  - All light specifications, location, designs and installations shall be approved by the Director of Public Works.

  - If street directed lighting is required by the Director of Public Works or the State Highway Administration it shall be located on the same or same style pole.

  - Where a building is directly adjacent to a quasi-public walkway, wall mounted lighting consistent in style and quality with the streetscape lighting may be substituted for streetlights.

- LED is preferred.

- Lighting shall meet dark sky standards.

- Lighting shall have a minimum color rendering index of 75.

- Lighting design shall achieve an even distribution across the sidewalk to 6 feet in height and not create dark shadows or glare.

## Site Furniture

Intent:  Use site furniture to create a unique visual identity for the crossroads and create inviting and comfortable streets that support diverse community members.

- Benches shall be durable, easily maintainable, and comfortable.

  - Benches within public streetscapes shall be approved by the Director of Public Works.

    - Along business streets, the Urbanscape “Dewart” bench is preferred.

    - Within park-like and leafy residential areas, the Urbanscape “Beverly Shores” is preferred.

  - Within retail streets benches shall be placed in the street furniture zone at a minimum of 1 per 100 linear feet and a minimum of one bench shall be installed per 1500 square feet of open space.

  - Cluster benches with other amenities such as other benches, waste receptacles, flower pots, etc.

  - Distribute benches so that there is a selection in the shade and in sun throughout the day.

  - Offset benches 24 inches from the pedestrian flow of traffic.

  - Do pave areas adjacent to 50% of benches to allow for wheelchairs.

  - Do not place most benches at more than a 90 degree angle towards each other.

- High quality, movable furniture is strongly encouraged where there is a management entity responsible for daily care and maintenance.

- Bicycle racks in the streetscape furniture zone shall coordinate with street furniture and be approved by the Director of Public Works.

  - Place bicycle racks near entrances to retail, office buildings, and residential structures, and bus stops.

- Trash and recycling cans shall be placed at corners and bus stops and shall be installed at the minimum rate of one set per three hundred linear feet of public or private sidewalk.

  - Receptacles to be placed in the right-of-way shall be approved by the Director of Public Works.

  - Trash and recycling cans shall conform to the style and quality established within the public right of way.

  - Recycling cans shall include instructions in English, Spanish, Amharic, and French at a minimum.

## Trees

Intent:

Create an inviting shopping environment of dappled shade, improve quality of life, provide traffic calming, reduce the heat island effect and stormwater run off, and sequester carbons.

- Street trees shall be large shade trees.

  - Trees shall provide a dappled and not overly heavy shade; be limbable at full growth to 12 feet in height, and branch upwards.

  - Trees in public right-of-ways and public improvement easements shall be approved by the City of Takoma Park Arborist and each street shall have a consistent species or cultivar.

  - Retail streets, avenues and boulevards (public or private) shall be defined with trees planted 20-25 feet on center.

  - All other streets shall be defined with tall shade trees planted 20-35 feet on center.

  - Private and public alleys shall be defined by trees planted a minimum of 35 feet on center.  Alley trees shall be tall shade trees unless overhead wires are located to the alley in which case they may be shorter shade trees.

  - Fastigiate trees may not be used as street trees.

- Plant trees along pathways on either side where feasible to create an allee.

- Where appropriate, plant trees on the west and south sides of buildings to reduce heat loads.

- Where a streetscape irrigation system is not installed, hose bibs shall be installed on the outside of new buildings in locations appropriate for watering street trees and landscaping.

- Tree coverage at ten years of growth shall meet the following minimums:

  - Gross lot area:  25%

  - Surface parking lots: 50%.

  - Parks, plazas, yards, shared green space: 50%.

  - With the exception of parking lots, the planting of offsite street trees within the district with a one year watering contract and guarantee may be substituted for onsite trees.

# LANDSCAPING AND HARDSCAPE

Intent:  Improve public safety and comfort, soften environment.

- Limit the use of shrubs taller than three feet in height to areas where they screen parking and taller than four feet in height where they soften walls.

- Sidewalks shall not be made of asphalt.

- Use seating, walls, and other elements to discourage pedestrian traffic within gardens and critical tree root zones.

- Paving shall be of high quality.

- Streetscape and sidewalks shall be of a continuous pattern and design across driveway entrances.

Intent:  Improve permeability, reduce negative environmental impacts, reduce carbon footprint.

- Grass lawns/turf is to be avoided except for shared use areas such as in a park or playing field.

- Plant slopes with groundcover.

- Select plants that have low water and pesticide needs, and generate minimum plant trimmings.

- Emphasize plant diversity, plants that are native to the region and microclimate, and those which naturally grow together and are self-sustaining (i.e. reseed and spread without much maintenance).

- Design landscapes to collect and absorb rainwater runoff (stormwater).

- Irrigation should be drip or seep and consider catchments to recycle rainwater for landscape irrigation where feasible.  Spray type irrigation is to be avoided.

- Include designated infrastructure with appropriate screening for onsite collection and composting of yard waste.

- Use heat retaining pavements in courtyards and plazas.

## Tree Planting Standards

Intent:   Improve the ability of trees to survive the urban environment and grow large enough to improve quality of life and the environment.

- All trees shall be planted in accordance with the landscape standards of this document.

- Provide tall shade trees with 1500 cubic feet of soil.

  - Soil shall have 20% organic material.

  - Soil shall be loose, not compacted, with the exception of the base for the tree root ball.

  - Under paving, Silva Cell or other City Arborist approved structure shall protect soil from compaction.

  - Soil at a depth greater than three feet below the top of the tree box shall not be included in the volume calculation.

  - Up to 40% of the volume may be overlapped and shared by a maximum of one additional tree on either side.

- Provide ornamental trees with 900 cubic feet of soil.

  - Soil shall have 20% organic material.

  - Soil shall be loose, not compacted, with the exception of the base for the tree root ball.

  - Silva Cell or other City Arborist approved structure shall support paving and protect soil underneath from compaction.

  - Soil at a depth greater than three feet below the top of the tree box shall not be included in the volume calculation.

  - Up to 40% of the volume may be overlapped and shared by a maximum of one additional tree on either side.